## Slide 1
Computer Organization and Architecture
Department of Computer Science and Engineering
IIT Kharagpur
Module 4
Design of Control Unit

## Slide 2: Design of Control Unit

## Slide 3: Instructions
Instructions are stored in main memory.
Program Counter (PC) points to the next instruction.
  MIPS32 instructions are 4 bytes (32 bits) long.
  All instructions starts from an address that is multiple of 4 (last 2 bits 00).
  Normally, PC is incremented by 4 to point to the next instruction.
  For branch, PC is loaded with the address of the target instruction.
0
4
8
12
instruction word
instruction word

## Slide 4: Addressing a Byte in Memory
Each byte in memory has a unique address.
  Memory is said to be byte addressable.
Typically the instructions are of 4 bytes, hence the instruction memory is addressed in terms of 4 bytes (word length = 32 bits).
When an instruction is executed, PC is incremented by 4 to point to the next instruction.
  In MIPS32, words are byte aligned.
  Every word (including instruction) starts from a memory address that is some multiple of 4 (i.e., last two bits are `00’).

## Slide 5: How an instruction Gets Executed?
repeat forever
// till power off or
// system failure
{
  Fetch instruction
  Decode instruction
  Execute instruction
  }
Fetch
Decode
Execute
Main Memory

## Slide 6: The Fetch-Execute Cycle
Fetch the next instruction from memory.
Decode the instruction.
Execute the operation.
  Get data from memory if needed (data not available in the processor).
  Perform the required operation on the data.
  May also store the result back in memory or register.

## Slide 7: Registers: PC and IR
Program Counter (PC) holds the address of the memory location containing the next instruction to be executed.
Instruction Register (IR) contains the current instruction being executed.
Basic processing cycle:
  Instruction Fetch (IF)
    IR ← Mem [PC]
  Considering the word length of the machine is 32 bits, the PC is incremented by 4 to point to the next instruction.
    PC ← PC + 4
  Carry out the operations specified in IR.

## Slide 8: Example: Add R1, R2
Address | Instruction
1000 | ADD R1, R2
1004 | MUL R3, R4
PC = 1000
MAR = 1000
PC = PC + 4 = 1004
MDR = “ADD R1, R2”
IR = “ADD R1, R2”
(Decode and finally execute)
R1 = R1 + R2
May require one or more steps depending on the target architecture.

## Slide 9: Requirement for Instruction Execution
The necessary registers must be present.
The internal organization of the registers must be known.
The data path must be known.
For instruction execution, a number of micro-operations are carried out on the data path.
  An instruction consists of several micro-operations or micro-instructions.
  Typically involves movement of data.

## Slide 10: Kinds of Data Movement
Broadly three types:
  Register to Register
  Register to ALU
  ALU to Register
Data movement is supported in the data path by:
  The Registers
  The Bus (single or multiple)
  The ALU temporary Register (Y and Z)

## Slide 11
Internal Processor Bus
PC
MAR
MDR
Y
IR
R0
R1
Rn-1
Instruction Decoding and Control Unit
Z
MEMORY
4
Function select
Select
ALU
Control signals
MUX
.
.
.
.
.
.
Carry-in
Single Bus Organization
General-purpose Registers

## Slide 12: Single Internal Bus Organization
All the registers and various units are connected using a single internal bus.
Registers R0-Rn-1 are general-purpose registers used for various purposes.
Registers Y and Z are used for storing intermediate results and never used by instructions explicitly.
The multiplexer selects either a constant 4 or output of register Y.
  When PC is incremented, a constant 4 has to be added.

## Slide 13
The instruction decoder and control unit is responsible for performing the actions specified by the instruction loaded into IR.
The decoder generates all the control signals in the proper sequence required to execute the instruction specified by the IR.
The registers, the ALU and the interconnecting bus are collectively referred to as the data path.
The control unit that generates the control signals in proper sequence is referred to as the control path.

## Slide 14: Kinds of Operations
Transfer of data from one register to another.
  MOVE R1, R2 // R1 = R2
Perform arithmetic or logic operation on data loaded into registers.
  ADD R1, R2 // R1 = R1 + R2
Fetch the content of a memory location and load it into a register.
  LOAD R1, LOCA // R1 = Mem[LOCA]
Store a word of data from a register into a given memory location.
  STOR LOCA, R1 // Mem[LOCA] = R1

## Slide 15: Three Bus Organization
A typical 3-bus architecture for the processor datapath is shown in the next slide.
  The 3-bus organization is internal to the CPU.
  Three buses allow three parallel data transfer operations to be carried out.
Less number of cycles required to execute an instruction compared to single bus organization.

## Slide 16
PC
MAR
MDR
IR
Instruction Decoder
A
L
U
Incrementer
Register File
4
Bus A
Bus B
Bus C
M
U
X
Memory
Address
Data
We assume that two register reads and one register write operations can be carried out in a single clock cycle.

## Slide 17: Organization of a Register
A register is used for temporary storage of data (parallel-in, parallel-out, etc.).
A register Ri typically has two control signals.
  Riin : used to load the register with data from the bus.
  Riout : used to place the data stored in the register on the bus.
Input and output lines of the register Ri are connected to the bus via controlled switches.
  If Riout is not selected, the register outputs are set in the high impedance state.
Register Ri
Riin
Riout

## Slide 18
Register Ri
Riin
Riout
When (Riin = 1), the data available on bus is loaded into Ri.
When (Riout = 1), the data from register Ri are placed on the bus.
Register Ri
Riin
Riout

## Slide 19: Register Transfer
R1in
Register R2
R2in
R2out
Register R1
R1out
MOVE R1, R2 // R1  R2
  Enable the output of R2 by setting R2out = 1.
  Enable the input of register R1 by setting R1in = 1.
  All operations are performed in synchronism with the processor clock.
    The control signals are asserted at the start of the clock cycle.
    After data transfer the control signals will return to 0.
  We write as T1: R2out , R1in
Time Step
Control Signals

## Slide 20: ALU Operation
Ri
Riin
Riout
Y
Yin
MUX
ALU
S
4
X
Z
X
Zin
Zout
X
X
X
ADD R1, R2 // R1 = R1 + R2
  Bring the two operands (R1 and R2) to the two inputs of the ALU.
    One through Y (R1) and another (R2) directly from internal bus.
  Result is stored in Z and finally transferred to R1.
  T1: R1out , Yin
  T2: R2out , SelectY, ADD, Zin
  T3: Zout , R1in

## Slide 21: Fetching a Word from Memory
The steps involved to fetch a word from memory:
  The processor specifies the address of the memory location where the data or instruction is stored (move to MAR).
  The processor requests a read operation.
    The information to be fetched can either be an instruction or an operand of the instruction.
  The data read is brought from the memory to MDR.
  Then it is transferred to the required register or ALU for further operation.

## Slide 22: Storing a Word into Memory
The steps involved to store a word into the memory:
  The processor specifies the address of the memory location where the data is to be written (move to MAR).
  The data to be written in loaded into MDR.
  The processor requests a write operation.
  The content of MDR will be written to the specified memory location.

## Slide 23: Connecting MDR to Memory Bus and Internal Bus
MDR
MDRin
MDRout
Internal processor bus
MDRinE
MDRoutE
Memory bus
Memory
MAR
MFC
Memory Function Complete

## Slide 24
Memory read/write operation:
  The address of memory location is transferred to MAR.
  At the same time a read/write control signal is provided to indicate the operation.
  For read, the data from memory data bus comes to MDR by activating MDRinE .
  For write, the data from MDR goes to memory data bus by activating the signal MDRoutE .
  When the processor sends a read request, it has to wait until the data is read from the memory and written into MDR.
  To accommodate the variability in response time, the process has to wait until it receives an indication from the memory that the read operation has been completed.
  A control signal called Memory Function Complete (MFC) is used for this purpose.
    When this signal is 1, indicates that the contents of the specified location is read and are available on the data line of the memory bus.
    Then the data can be made available to MDR.

## Slide 25: Timing Diagram for Read Operation
Computer Organization, Fifth Edition, Carl Hamacher, Zvonko Vranesic, Safwat Zaky.
MAR ← R2
Start a Read operation on the memory bus
Wait for the MFC response from the memory
Load MDR from the memory
R1 ← MDR
Control steps:
  1. R2out , MARin , Read
  2. MDRinE , WMFC
  3. MDRout , R1in

## Slide 26: Fetch a word: MOVE R1, (R2)
MAR ← R2
Start a Read operation on the memory bus
Wait for the MFC response from the memory
Load MDR from the memory
R1 ← MDR
Control steps:
  R2out , MARin , Read
  MDRinE , WMFC
  MDRout , R1in

## Slide 27: Fetch a word: MOVE R1, (R2)
MAR ← R2
Start a Read operation on the memory bus
Wait for the MFC response from the memory
Load MDR from the memory
R1 ← MDR
Control steps:
  R2out , MARin , Read
  MDRinE , WMFC
  MDRout , R1in

## Slide 28: Fetch a word: MOVE R1, (R2)
MAR ← R2
Start a Read operation on the memory bus
Wait for the MFC response from the memory
Load MDR from the memory
R1 ← MDR
Control steps:
  R2out , MARin , Read
  MDRinE , WMFC
  MDRout , R1in

## Slide 29: Fetch a word: MOVE R1, (R2)
MAR ← R2
Start a Read operation on the memory bus
Wait for the MFC response from the memory
Load MDR from the memory
R1 ← MDR
Control steps:
  R2out , MARin , Read
  MDRinE , WMFC
  MDRout , R1in

## Slide 30: Store a word: MOVE (R1), R2
MAR ← R1
MDR ← R2
Start a Write operation on the memory bus
Wait for the MFC response from the memory
Control steps:
  R1out , MARin
  R2out, MDRin , Write
  MDRoutE , WMFC

## Slide 31: Store a word: MOVE (R1), R2
MAR ← R1
MDR ← R2
Start a Write operation on the memory bus
Wait for the MFC response from the memory
Control steps:
  R1out , MARin
  R2out, MDRin , Write
  MDRoutE , WMFC

## Slide 32: Store a word: MOVE (R1), R2
MAR ← R1
MDR ← R2
Start a Write operation on the memory bus
Wait for the MFC response from the memory
Control steps:
  R1out , MARin
  R2out, MDRin , Write
  MDRoutE , WMFC

## Slide 33: Store a word: MOVE (R1), R2
MAR ← R1
MDR ← R2
Start a Write operation on the memory bus
Wait for the MFC response from the memory
Control steps:
  R1out , MARin
  R2out, MDRin , Write
  MDRoutE , WMFC

## Slide 34: Execution of a Complete Instruction
ADD R1, R2 // R1 = R1 + R2
T1: PCout, MARin, Read, Select4, ADD, Zin
T2: Zout, PCin, Yin, MDRinE ,WMFC
T3: MDRout, IRin
T4: R1out, Yin, SelectY
T5: R2out, ADD, Zin
T6: Zout, R1in
Ri
Riin
Riout
Y
Yin
MUX
ALU
S
4
X
Z
X
Zin
Zout
X
X
X

## Slide 35: Execution of a Complete Instruction
ADD R1, R2 // R1 = R1 + R2
T1: PCout, MARin, Read, Select4, ADD, Zin
T2: Zout, PCin, Yin, MDRinE ,WMFC
T3: MDRout, IRin
T4: R1out, Yin, SelectY
T5: R2out, ADD, Zin
T6: Zout, R1in

## Slide 36: Execution of a Complete Instruction
ADD R1, R2 // R1 = R1 + R2
T1: PCout, MARin, Read, Select4, ADD, Zin
T2: Zout, PCin, Yin, MDRinE ,WMFC
T3: MDRout, IRin
T4: R1out, Yin, SelectY
T5: R2out, ADD, Zin
T6: Zout, R1in

## Slide 37: Execution of a Complete Instruction
ADD R1, R2 // R1 = R1 + R2
T1: PCout, MARin, Read, Select4, ADD, Zin
T2: Zout, PCin, Yin, MDRinE ,WMFC
T3: MDRout, IRin
T4: R1out, Yin, SelectY
T5: R2out, ADD, Zin
T6: Zout, R1in

## Slide 38: Execution of a Complete Instruction
ADD R1, R2 // R1 = R1 + R2
T1: PCout, MARin, Read, Select4, ADD, Zin
T2: Zout, PCin, Yin, MDRinE ,WMFC
T3: MDRout, IRin
T4: R1out, Yin, SelectY
T5: R2out, ADD, Zin
T6: Zout, R1in

## Slide 39: Execution of a Complete Instruction
ADD R1, R2 // R1 = R1 + R2
T1: PCout, MARin, Read, Select4, ADD, Zin
T2: Zout, PCin, Yin, MDRinE ,WMFC
T3: MDRout, IRin
T4: R1out, Yin, SelectY
T5: R2out, ADD, Zin
T6: Zout, R1in

## Slide 40: Execution of a Complete Instruction
ADD R1, R2 // R1 = R1 + R2
T1: PCout, MARin, Read, Select4, ADD, Zin
T2: Zout, PCin, Yin, MDRinE ,WMFC
T3: MDRout, IRin
T4: R1out, Yin, SelectY
T5: R2out, ADD, Zin
T6: Zout, R1in
SelectY can be placed in T4 or T5 since mux is a combinatorial circuit and its output will be generated almost instantly.

## Slide 41: Example for a Three Bus Organization
SUB R1, R2, R3 // R1 = R2 – R3
T1: PCout, R = B, MARin , READ, IncPC
T2: WMFC
T3: MDRoutB , R = B, IRin
T4: R2outA , R3outB , SelectA, SUB, R1in , End
R = B means that the ALU function is selected such that data on Bus-B is transferred to the ALU output (i.e., Bus-C).

## Slide 42: Micro-operations Examples

## Slide 43: Introduction
We select a set of 12 instructions.
Discuss the control signals required to execute these instructions on the single-bus processor architecture.

## Slide 44: The set of 12 instructions chosen
ADD R1, R2 // R1 = R1 + R2
ADD R1, LOCA // R1 = R1 + Mem[LOCA]
LOAD R1, LOCA // R1 = Mem[LOCA]
STORE LOCA, R1 // Mem[LOCA] = R1
MOVE R1, R2 // R1 = R2
MOVE R1, #10 // R1 = 10
BR LOCA // PC = LOCA
BZ LOCA // PC = LOCA if Zero flag is set
INC R1 // R1 = R1 + 4
DEC R1 // R1 = R1 – 4
CMP R1, R2 // R1 – R2
HALT // Machine Halt

## Slide 45: 1. ADD R1, R2 (R1 = R1 + R2)
T1: PCout, MARin, Read, Select4, Add, Zin
T2: Zout, PCin, Yin, MDRinE ,WMFC
T3: MDRout, IRin
T4: R1out, Yin
T5: R2out, SelectY, Add, Zin
T6: Zout, R1in, End

## Slide 46: 2. ADD R1, LOCA (R1 = R1 + Mem[LOCA])
T1: PCout, MARin, Read, Select4, Add, Zin
T2: Zout, PCin, Yin, MDRinE ,WMFC
T3: MDRout, IRin
T4: Address field of IRout, MARin, Read
T5: R1out, Yin, MDRinE ,WMFC
T6: MDRout, SelectY, Add, Zin
T7: Zout, R1in, End

## Slide 47: 3. LOAD R1, LOCA (R1 = Mem[LOCA])
T1: PCout, MARin, Read, Select4, Add, Zin
T2: Zout, PCin, Yin, MDRinE ,WMFC
T3: MDRout, IRin
T4: Address field of IRout, MARin, Read
T5: MDRinE ,WMFC
T6: MDRout, R1in, End

## Slide 48: 4. STORE LOCA, R1 (Mem[LOCA] = R1)
T1: PCout, MARin, Read, Select4, Add, Zin
T2: Zout, PCin, Yin, MDRinE ,WMFC
T3: MDRout, IRin
T4: Address field of IRout, MARin
T5: R1out, MDRin, Write
T6: MDRoutE, WMFC, End

## Slide 49: 5. MOVE R1, R2 (R1 = R2)
T1: PCout, MARin, Read, Select4, Add, Zin
T2: Zout, PCin, Yin, MDRinE ,WMFC
T3: MDRout, IRin
T4: R2out, R1in, END

## Slide 50: 6. MOVE R1, #10 (R1 = 10)
T1: PCout, MARin, Read, Select4, Add, Zin
T2: Zout, PCin, Yin, MDRinE ,WMFC
T3: MDRout, IRin
T4: Immediate field of IRout, R1in, END

## Slide 51: 7. BRANCH Label (PC = PC + offset)
T1: PCout, MARin, Read, Select4, Add, Zin
T2: Zout, PCin, Yin, MDRinE ,WMFC
T3: MDRout, IRin
T4: Offset-field-of-IRout, SelectY, Add, Zin
T5: Zout, PCin, End

## Slide 52: 8. BZ Label (if Z=1, PC = PC + offset)
T1: PCout, MARin, Read, Select4, Add, Zin
T2: Zout, PCin, Yin, MDRinE ,WMFC
T3: MDRout, IRin
T4: Offset-field-of-IRout, SelectY, Add, Zin, If Z=0 then End
T5: Zout, PCin, End

## Slide 53: 9. INC R1 (R1 = R1 + 4)
T1: PCout, MARin, Read, Select4, Add, Zin
T2: Zout, PCin, Yin, MDRinE ,WMFC
T3: MDRout, IRin
T4: R1out, Select4, Add, Zin
T5: Zout, R1in, End

## Slide 54: 10. DEC R1 (R1 = R1 – 4)
T1: PCout, MARin, Read, Select4, Add, Zin
T2: Zout, PCin, Yin, MDRinE ,WMFC
T3: MDRout, IRin
T4: R1out, Select4, Sub, Zin
T5: Zout, R1in, End

## Slide 55: 11. CMP R1, R2
T1: PCout, MARin, Read, Select4, Add, Zin
T2: Zout, PCin, Yin, MDRinE ,WMFC
T3: MDRout, IRin
T4: R1out, Yin
T5: R2out, SelectY, Sub, Zin, End

## Slide 56: 12. HALT
T1: PCout, MARin, Read, Select4, Add, Zin
T2: Zout, PCin, Yin, MDRinE ,WMFC
T3: MDRout, IRin
T4: END

## Slide 57: ADD (R3), R1

## Slide 58: Practice Assignment 1
Write down the micro-operations for the 12 instructions with respect to the 3-bus architecture.
Assumption: Two register read and one register write operations can be carried out concurrently in a single time step.

## Slide 59: Practice Assignment 2
Complete the following table for both the 1-bus and 3-bus architectures.
  Ins-1 to Ins-12 indicates the instructions.
  The entries in the table will contain the corresponding micro-operations.
 | Ins-1 | Ins-2 | Ins-3 | Ins-4 | Ins-5 | Ins-6 | Ins-7 | Ins-8 | Ins-9 | Ins-10 | Ins-11 | nIs-12
T1 |  |  |  |  |  |  |  |  |  |  |  | 
T2 |  |  |  |  |  |  |  |  |  |  |  | 
T3 |  |  |  |  |  |  |  |  |  |  |  | 
T4 |  |  |  |  |  |  |  |  |  |  |  | 
T5 |  |  |  |  |  |  |  |  |  |  |  | 
T6 |  |  |  |  |  |  |  |  |  |  |  | 
T7 |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 60: Hardwired and Microprogrammed Control Unit Design

## Slide 61: Introduction
To execute an instruction, the processor must generate control signals for the data path in proper sequence.
  Example: ADD R1, R2
    R1out, Yin, SelectY
    R2out, ADD, Zin
    Zout, R1in
Two alternate approaches:
  Hardwired control unit design
  Microprogrammed control unit design

## Slide 62: Hardwired Control Unit Design
What does the control unit do?
  It generates the control signals in proper sequence so as to execute any given instruction.
  We have already seen some example control signals for some instructions.
Basic question?
  For an instruction Ik and time step Tm, what are the control signals that need to be generated?
What is hardwired control unit?
  The control signals are generated by specific hardware circuits that cannot be easily modified.
  It is fixed or hardwired for a given <architecture, ISA> pair.

## Slide 63: Overall Schematic Diagram
External
inputs
Encoder
CLK
Clock
counter
End
Condition
Codes flags
Step decoder
Control step
IR
T
1
T
2
T
n
:
:
:
..
INSm
INS2
INS1
..
Run
..
RESET
Control signals
Instruction Decoder

## Slide 64
Basic Principle of Operation:
  The step decoder provides separate signal for each step (T1, T2, T3, etc.)..
  The instruction decoder has separate output lines for each machine instruction.
  For any instruction loaded in IR, one of the output line INS1, …, INSm is set to 1 (others are 0).
  The input signals to the encoder block are combined to generate individual control signals.
  The signal RUN causes the counter to be incremented by 1, stops counting when RUN = 0. This is needed when the WMFC signal is issued, causing the processor wait for a memory reply.
Assumption:
  Each time step is completed in one clock cycle.
  The control step counter keeps track of the time step.

## Slide 65
The control signals are determined by the following information:
  Content of control step counter
  Content of instruction register
  Content of conditional code flags
  External input signals such as WMFC

## Slide 66
The Encoder circuit is a combinational circuit which generates control signals depending on the inputs provided.
The Step Decoder generates separate signal lines for each step in the control sequence (T1, T2, T3, etc.).
  Depending on maximum steps required for an instruction, the step decoder is designed.
  If a maximum of 10 steps are required, then a 4 x 16 step decoder is used.
Among the total set of instructions, the instruction decoder is used to select one of them. (That particular line will be 1 and rest will be 0).
  If a maximum of 100 instructions are present in the ISA, then a 7 x 128 instruction decoder is used.

## Slide 67
At every clock cycle the RUN signal is used to increment the counter by one.
  When RUN is 0 the counter stops counting.
  This signal is needed when WMFC is issued.
The END signal starts a new instruction.
  It resets the control step counter to its starting value.
The sequence of operations carried out by the control unit is determined by the wiring of the logic elements and hence it is named hardwired.
  This approach of control unit design is fast but limited to the complexity of instruction set that is implemented.

## Slide 68: Generation of Control Signals (Hardwired Control)

## Slide 69
ADD R1,R2
ADD R1,LOCA
LOAD R1,LOCA
BR Label
INC R1

## Slide 70
 | I1 | I2 | I3 | I4 | I5
T1 | PCout, MARin, Read, Select4, ADD, Zin | PCout, MARin, Read, Select4, ADD, Zin | PCout, MARin, Read, Select4, ADD, Zin | PCout, MARin, Read, Select4, ADD, Zin | PCout, MARin, Read, Select4, ADD, Zin
T2 | Zout, PCin, Yin, WMFC | Zout, PCin, Yin, WMFC | Zout, PCin, Yin, WMFC | Zout, PCin, Yin, WMFC | Zout, PCin, Yin, WMFC
T3 | MDRout, IRin | MDRout, IRin | MDRout, IRin | MDRout, IRin | MDRout, IRin
T4 | R1out, Yin | Address field of IRout, MARin, Read | Address field of IRout, MARin, Read | Offset field of IRout, SelectY, ADD, Zin | R1out, Select4, ADD, Zin
T5 | R2out, SelectY, ADD, Zin | R1out, Yin, WMFC | WMFC | Zout, PCin, END | Zout, R1in, END
T6 | Zout, R1in, END | MDRout, SelectY, ADD, Zin | MDRout, R1in, END |  | 
T7 |  | Zout, R1in, END |  |  | 
ADD R1,R2
INC R1
LOAD R1,LOCA
BR Label
ADD R1,LOCA

## Slide 71: Logic for Generation of Some of the Control Signals
PCin = T2 + T5.I4
PCout = T1
MARin = T1 + T4.(I2 + I3)
Zin = T1 + T4.(I4 + I5) + T6.I2
Zout = T2 + T5.(I4 + I5) + T6.I1 + T7.I2
MDRout = T3 + T6.(I2 + I3)
IRin = T3
Yin = T2 + T4.I1 + T5.I2
Select4 = T1 + T4.I5
SelectY = T4.I4 + T5.I1 + T6.I2
END = T5.(I4 + I5) + T6.(I1 + I3) + T7.I2
Rxin = T5.I5 + T6.(I1 + I3) + T7.I2
Rxout = T4.(I1 + I5) + T5.(I1 + I2)
WMFC = T2 + T5.(I2 + I3)

## Slide 72: Design of the Encoder Block
Implement the logic functions to generate the control signals.
  Using logic gates or any other hardware module.
This method of generating control signals is very fast.

## Slide 73: Practice Assignment 3
Design the hardwired control unit for the 12 instructions as given for:
  1-bus architecture
  3-bus architecture

## Slide 74: Generation of Control Signals (Microprogrammed Control)

## Slide 75: Microprogrammed Control Unit Design
Control signals are generated by a program similar to machine language program.
A Control Store (CS) stores the microroutines for all instructions of an ISA.
The sequence of steps corresponding to the control sequence of a machine instruction is the microroutine.
Each sequence of steps is a Control Word (CW) whose individual bits represent the various control signals.
Individual control words in a microroutine are called microinstructions.

## Slide 76
Control Word (CW)
IR
Starting and Branch Address Generator
μPC
Clock
Control Store
External Inputs
Condition Codes

## Slide 77
Control-unit generates the control signals for an instruction by sequentially reading CWs of corresponding microroutine from CS.
The micro-program counter (μPC) is used to read CWs sequentially from CS.
Every time a new instruction is loaded into IR, output of Starting Address Generator is loaded into μPC.
Then, μPC is automatically incremented by clock causing successive microinstructions to be read from CS.
Control Word (CW)
IR
Starting and Branch Address Generator
μPC
Clock
Control Store
External Inputs
Condition Codes

## Slide 78: Control Store Contents for “ADD R1, R2”
Micro- instr. | … | PCin | PCout | MARin | Read | MDRout | IRin | Yin | Select | Add | Zin | Zout | R1out | R1in | R2out | WMFC | End | …
1 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
2 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0
3 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
4 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
5 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0
6 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 1 | 0

## Slide 79: Control Store Contents for “BR Label”
Micro- instr. | … | PCin | PCout | MARin | Read | MDRout | IRin | Yin | Select | Add | Zin | Zout | IRout | WMFC | End | …
1 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0
2 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0
3 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
4 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 0
5 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0

## Slide 80: Using Conditional Branching
The previous organization cannot handle the situation when the control unit is required to check the status of the condition codes or external inputs to choose between alternative courses of action.
Possible solution:
  Use conditional branch microinstruction.
  An example is shown on the next slide.

## Slide 81
Address
Microinstruction
0
PC
out
,
MAR
in
,
Read,
Select4,
Add,
Z
in
1
Z
out
,
PC
in
,
Y
in
,
WMFC
2
MDR
out
,
IR
in
3
Branch
to
starting
address
of
appropriate
microroutine
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
25
If
Z=0,
then
branch
to
microinstruction 0
26
Offset-field-of-IR
out
,
SelectY,
Add,
Z
in
27
Z
out
,
PC
in
,
End

## Slide 82
Control Word (CW)
IR
Starting and Branch Address Generator
μPC
Clock
Control Store
External Inputs
Condition Codes

## Slide 83: Microprogram Sequencing
If all microprograms require only straightforward sequential execution of microinstructions except for branches, letting a μPC govern the sequencing would be efficient.
However, two disadvantages:
  Having a separate microroutine for each machine instruction results in a large total number of microinstructions and a large control store.
  Longer execution time because it takes more time to carry out the required branches.

## Slide 85: Microinstructions with Next-Address Field
The microprogram requires several branch microinstructions, which perform no useful operation in the datapath.
An alternative approach:
  Include an address field as a part of every microinstruction to indicate the location of the next microinstruction to be fetched.
Pros: separate branch microinstructions are virtually eliminated; few limitations in assigning addresses to microinstructions.
Cons: additional bits required for the address field.

## Slide 86
μPC
From the instruction opcode, some constant bits are appended (both at the left and right) to get the starting address of the corresponding micro-routine in control store.

## Slide 87: Illustrative Example
Some example instructions and their 4-bit opcodes:
Opcodes Starting Address of Micro-routine
  ADD 0010 0 0010 000
  SUB 0011 0 0011 000
  LOAD 0100 0 0100 000
  STORE 0101 0 0101 000
  BR 1010 0 1010 000

## Slide 88: Practice Assignment 4
Design the microprogrammed control unit for the 12 instructions as given for the 1-bus architecture.
In particular, show the micro-routines for the various instructions, and the detailed contents of CS.

## Slide 89: Horizontal versus Vertical Microinstruction Encoding
Broadly there are two alternate schemes to code the control signals in the control memory.
  Horizontal Micro-instruction Encoding
    Each control signal is represented by a bit in the micro-instruction.
    Fewer control store words, with more bits per word.
  Vertical Micro-instruction Encoding
    Each control word represents a single micro-instruction in encoded form.
    k-bit control word can support up to 2k micro-instructions.
    More control store words, with fewer bits per word.

## Slide 90
There can be a tradeoff between horizontal and vertical micro-instruction encoding.
  Sometimes referred to as Diagonal Micro-instruction Encoding.
  The control signals are grouped into sets S1, S2, etc., such that the control signals within a set are mutually exclusive.
Summary:
  Horizontal encoding supports unlimited parallelism among micro-instructions.
  Vertical encoding supports strictly sequential execution of micro-instructions.
  Diagonal encoding does not sacrifice the required level of parallelism, but uses less number of bits per control word as compared to horizontal encoding.

## Slide 91: (a) Horizontal Micro-instruction Encoding
c1
c2
c3
c4
ck
…
Control Signals
Suppose that there are k control signals: c1, c2, …, ck.
In horizontal encoding, every control word stored in control memory (CM) consists of k bits, one bit for every control signal.
Several bits in a control word can be 1:
  Parallel activation of several micro-operations in a single time step.
0
1
0
1
0
1
 c2, c4 and c5 are activated together

## Slide 92
Advantage:
  Unlimited parallelism is possible in the activation of the micro-operations.
Disadvantage:
  Size of the control memory is large (word size is much longer).
  Cost of implementation is higher.

## Slide 93: Example
fefew

## Slide 94: (b) Vertical Micro-instruction Encoding
m-bit word
DECODER
…
c1
c2
c3
c4
ck
Again consider that there are k control signals: c1, c2, …, ck.
We encode the control signals in an m-bit word in the control memory, where k ≤ 2m.
Depending on the m-bit control word, exactly one control signal will be activated (= 1), while all others will remain de-activated (= 0).
  At most one control signal can be activated in a time step.

## Slide 95
Advantage:
  Requires much smaller word size in control memory.
  Low cost of implementation.
Disadvantage:
  More than one control signals cannot be activated at a time.
  Requires sequential activation of the control signals, and hence more number of time steps.

## Slide 96: (c) Diagonal Micro-instruction Encoding
Suppose we group the set of k control signals into s groups, containing k1, k2, …, ks signals.
We encode the control signals in groups as shown, where ki ≤ 2mi.
  Within a group, at most one control signal can be activated in a time step.
  Parallelism across groups is allowed.
m1-bit
m2-bit
m3-bit
ms-bit
…
DECODER
DECODER
DECODER
…
…
…
c1,1
c1,k1
cm,1
cm,ks
c2,1
c2,k2

## Slide 97
Advantages:
  Maximum parallelism as required by the micro-programs can be supported.
  Word size of control memory is less than that for horizontal encoding.
  Used in practice.
Disadvantages:
  Multiple decoders (though smaller in sizes) are required.

## Slide 98: Example 1
Suppose there are 100 control signals in a processor data path.
  For horizontal encoding, control word size = 100 bits.
  For vertical encoding, control word size = log2 100 = 7 bits.
  For diagonal encoding, suppose after analysis of the micro-programs, we divide the control signals into 5 groups, containing 25, 15, 40, 5 and 15 control signals respectively.
    We have: m1 = 5, m2 = 4, m3 = 6, m4 = 3, m5 = 4
    Control word size = 5 + 4 + 6 + 3 + 4 = 22 bits.
25 ≤ 25 15 ≤ 24
40 ≤ 26 5 ≤ 23
15 ≤ 24

## Slide 99: A Single Cycle Data Path

## Slide 100: A small set of instructions

## Slide 101: The instruction Set
Copy
Arithmetic
Logic
Memory Access
Control Transfer

## Slide 102: The Micro Mips ISA

## Slide 103: Instruction Execution Unit

## Slide 104: The Instruction Format
6 bits
5 bits
5 bits
5 bits
5 bits
6 bits
op
rs
rt
rd
sh
fn
Operand.offset,16 bits
imm
Opcode
Source 1
or base
Source 2
or dest
Destination
Unused
Opcode ext
jta
jump target address

## Slide 105: Abstraction of Instruction Execution Unit
NEXT ADDRESS
ALU
REG
FILE
PC
INSTR
CACHE
DATA CACHE
CONTROL UNIT
rs,rt,rd
imm
(rs)
(rt)
jta
Addr
Data
op
fn

## Slide 106: Register File
FF
FF
FF
FF
Write Data
Write Address
Write
Enable
Read
Enable
Read Address 0
Read Address 1
Read
data 0
Read
data 1
2h k-bit registers
MUXES
Decoder

## Slide 107: The ALU Architecture
ALU
XOR
LOGIC
XOR
Overflow=
x
y
Add’
/Sub
AND 00
OR 01
XOR 10
NOR 11
Pad 16 0s
fn:
00: lui
01 Set less
10 Arithmetic
11 Logic
MSB: 0 or 1
LogicFn
FnClass
cin
y or y’
c31
c32

## Slide 108: Execution Steps for R-type ALU Instructions
Read contents from rs and rt, and pass them to the ALU.
Control the ALU to perform the correct operation, according to the “func”-value of the Instruction.
Write the output of the ALU in register rd.

## Slide 109: Execution Steps for I-type ALU Instructions
Contents of rs and immediate value in the instruction are forwarded as inputs to the ALU.
Control the ALU to perform appropriate function.
Result is stored in the register rt (rather than rd in case of R-type instructions).

## Slide 110: Execution Steps for I-type Memory Instructions
Read contents of rs.
Add the contents of rs to signed extended immediate value in the instruction to form a memory address.
Read from or write to the memory location computed thus.
In case of lw, place the result in rt.
In case of sw, copy the result from rt.

## Slide 111: Register Access and ALU
ALU
REG
FILE
PC
INSTR
CACHE
rs
ALUimm
(rs)
(rt)
rt
rt
rd
31
RegDst
RegWrite
(rs)
(rt)
imm
ALUFunc

## Slide 112: Writing of the ALU output
ALU
REG
FILE
rs
ALUimm
(rs)
(rt)
rt
rt
rd
31
RegDst
RegWrite
(rs)
(rt)
imm
DATA CACHE
IncrPC
ALUFunc
Data
Read
Data
Write
RegInData
Data
Addr
Data
In
SE
16
32

## Slide 113: A single cycle data path

## Slide 115: The Next Address Architecture
Adder
Branch
Condition
Checker
(rt)
(rs)
BrType
(PC)31:2
BrTrue
IncrPC
jta
4 MSBs
of PC
26 bits
30 bits
SE
16 bits
SysCallAddr
Next PC
PCSrc
1

## Slide 116: Slightly Modified Branching and jumping (Next Address Logic)

## Slide 117: Pseudo-Direct Addressing
Consider a program:
0x1000_0000 LD R1, 0(R2)
0x1000_0100 J Label //Instruction: 0x08000440
0x1000_1000 …
Label: 0x1000_1100 …
Why does this work?

## Slide 118: Pseudo-Direct Addressing
Consider a program:
0x1000_0000 LD R1, 0(R2)
0x1000_0100 J Label //Instruction: 0x08000440
0x1000_1000 …
Label: 0x1000_1100 …
Why does this work?

## Slide 119: Lets move the code to a different memory location
Consider a program:
0x2000_0000 LD R1, 0(R2)
0x2000_0100 J Label //Instruction: 0x08000440
0x2000_1000 …
Label: 0x2000_1100 …
Does this work?

## Slide 120: Lets move the code to a different memory location
Consider a program:
0x2000_0000 LD R1, 0(R2)
0x2000_0100 J Label //Instruction: 0x08000440
0x2000_1000 …
Label: 0x2000_1100 …
Does this work?

## Slide 121: Partitions a 4GB address space…

## Slide 122: Pseudo-Direct Addressing
A pseudo-direct jump can reach up to instructions inside the current 256 MB region.
That is about 67 million instructions maximum per region.

## Slide 123: Deriving the Control Signals

## Slide 124: Single Cycle Data Path

## Slide 125: Control Signals in Single Cycle Data Path
101010

## Slide 126: Control Signal Settings: Repeated for Reference

## Slide 127: Generating Control Signals
The control signals are a function of op and fn fields.
One can express the control signals as a function of the op and fn bits.
  It is quite easy
However, the demerit of such an approach is if the instruction set is modified, or if we add new instructions, the entire control unit needs to be redesigned.

## Slide 128: The Decoder based control unit
op
1
fn
RtypeInst
bltzInst
jInst
jalInst
beqInst
bneInst
addiInst
sltiInst
andiInst
oriInst
xoriInst
luiiInst
lwInst
swInst
42
0
1
2
3
4
5
8
10
12
13
14
15
35
43
jrInst
syscallInst
addInst
subInst
andInst
orInst
xorInst
norInst
sltInst
8
12
32
34
36
37
38
39
6
6

## Slide 129: Expressing the Control Signals
Auxiliary signals:
  arithInst=addInst V subInst V sltInst V addiInst V sltiInst
  logicInst=andInst V orInst V xorInst V norInst V andiInst V oriInst V xoriInst
  immInst = luiInst V addiInst V sltiInst V andiInst V oriInst V xoriInst
Some Control Signals:
  RegWrite=luiInst V arithInst V logicInst V lwInst V jalInst
  ALUSrc=ImmInst V lwInst V swInst

## Slide 130: Performance of the Single Cycle Architecture
The above design of control circuit is a stateless and combinational design.
Each new instruction is read from the PC, and is executed in one single clock.
  Thus CPI=1
The clock cycle is determined by the longest instruction.

## Slide 131: Performance Estimation for Single-Cycle MicroMIPS
The MicroMIPS data path unfolded (by depicting the register write step as a separate block) so as to better visualize the critical-path latencies.
Instruction access 2 ns
Register read 1 ns
ALU operation 2 ns
Data cache access 2 ns
Register write 1 ns
Total 8 ns
Single-cycle clock = 125 MHz
R-type 44% 6 ns
Load 24% 8 ns
Store 12% 7 ns
Branch 18% 5 ns
Jump 2% 3 ns
Weighted mean  6.36 ns

## Slide 132: lw is the longest instruction
lw execution includes all the possible steps:
  Instruction Access: 2 ns
  Register Read: 1 ns
  ALU operation: 2 ns
  Data Cache Access: 2 ns
  Register Write-back:1 ns
  Total: 8 ns
  Thus a clock frequency of 125 MHz suffices.
  So, for 1 instruction, (1/125) x 10-6 sec
  Thus, 125 Million Instructions are executed per second (125 MIPS)

## Slide 133: Obtaining better performance
Note that the average instruction time is less, depends on the type of instruction, and their percentages in an application.
Rtype 44% 6 ns No data cache
Load 24% 8 ns
Store 12% 7ns No register write-back
Branch 18% 5ns Fetch+Register Read+Next-addr formation
Jump 2% 3ns Fetch + Instruction Decode
Weighted average = 6.36 ns
So, with a variable cycle time implementation, the performance is 157 MIPS
However, this is not possible.
We see that a single cycle implementation has a poor performance.

## Slide 134: Summary
Clock cycle is determined by the slowest instruction.
If the MIPS ISA includes more complex instructions, the disadvantage is more.
  For example if we add a MULT/DIV instruction by k times, then all operations need to be slowed down by k times.
  Thus MIPS does the MIPS/DIV instruction to a separate block (than the ALU block), with separate registers Hi and Lo.
    sufficient time is kept to write back the results to the register file