## Slide 1
Computer Organization and Architecture
Department of Computer Science and Engineering
IIT Kharagpur
Module 6 (Part 2)
Design of Memory Subsystems

## Slide 2: Memory Interfacing and Addressing

## Slide 3: Memory Interfacing
Basic problem:
  Interfacing one of more memory modules to the processor.
  We assume a single level memory at present (i.e. no cache memory).
Questions to be answered:
  How the processor address and data lines are connected to memory modules?
  How are the addresses decoded?
  How are the memory addresses distributed among the memory modules?
  How to speed up data transfer rate between processor and memory?

## Slide 4
PRIMARY
MEMORY
PROCESSOR
MA R
MD R
Address
Data
Control
The processor’s view of memory
Typical interface of a memory module.
Real chip may contain more signal lines (e.g. DRAM).
RD/WR’
MEMORY
(2n x m memory module)
n-bit address bus
m-bit data bus
CS’

## Slide 5: A Note About the Memory Interface Signals
The data signals of a memory module (RAM) are typically bidirectional.
  Some memory chips may have separate data in and data out lines.
For memory READ operation:
  Address of memory location is applied to address lines.
  RD/WR’ control signal is set to 1, and CS’ is set to 0.
  Data is read out through the data lines after memory access time delay.
For memory WRITE operation:
  Address of memory location is applied to address lines, and the data to be written to data lines.
  RD/WR’ control signal is set to 0, and CS’ is set to 0.

## Slide 6
Why is CS’ signal required?
  To handle multiple memory modules interfacing problem.
  We typically select only one out of several memory modules at a time.
What happens when CS’ = 1?
  When a memory module is not selected, the data lines are set to the high impedance state (i.e. electrically disconnected).
  An example scenario is shown.
RD/WR’
MEMORY
(2n x m)
Address
CS’ = 0
RD/WR’
MEMORY
(2n x m)
Address
m-bit data bus
CS’ = 1
SELECTED

## Slide 7: An Example Memory Interfacing Problem
Consider a MIPS32 like processor with a 32-bit address.
  Maximum memory that can be connected is 232 = 4 Gbytes.
  Assume that the processor data lines are 8 bits.
Assume that memory chips (RAM) are available with size 1 Gbyte.
  30 address lines and 8 data lines.
  Low-order 30 address lines (A29-A0) are connected to the memory modules.
We want to interface 4 such chips to the processor.
  Total memory of 4 Gbytes.

## Slide 8
MEMORY M0
(1G x 8)
MEMORY M1
(1G x 8)
MEMORY M2
(1G x 8)
MEMORY M3
(1G x 8)
PROCESSOR
A29 – A0
D7 – D0
2 x 4
Decoder
A30
A31
CS0’
CS1’
CS2’
CS3’
CS0’
RD/WR’
CS1’
RD/WR’
CS2’
RD/WR’
CS2’
RD/WR’

## Slide 9
High order address lines (A31 and A30) select one of the memory modules.
When is M0 selected?
  Address is: 0 0 x x x x x x x x x x x x x x x x x x x x x x x x x x x x x x
  Range of addresses is: 0x00000000 to 0x3FFFFFFF
When is M1 selected?
  Address is: 0 1 x x x x x x x x x x x x x x x x x x x x x x x x x x x x x x
  Range of addresses is: 0x40000000 to 0x7FFFFFFF
When is M2 selected?
  Address is: 1 0 x x x x x x x x x x x x x x x x x x x x x x x x x x x x x x
  Range of addresses is: 0x80000000 to 0xBFFFFFFF
When is M3 selected?
  Address is: 1 1 x x x x x x x x x x x x x x x x x x x x x x x x x x x x x x
  Range of addresses is: 0xC0000000 to 0xFFFFFFFF

## Slide 10
An observation:
  Consecutive block of bytes are mapped to the same memory module.
  For MIPS32, we have to access 32 bits (4 bytes) of data in parallel, which requires four sequential memory accesses here.
  We shall look at an alternate memory organization later that would make this possible.
    Called memory interleaving.

## Slide 11: Another Example
Use 1K x 4 memory modules to build a 8K x 8 memory system.

## Slide 12: Improved Memory Interface for MIPS32
We make small changes in the organization so that 32-bits of data can be fetched in a single memory access cycle.
  Exploit the concept of memory interleaving.
  Consecutive bytes are mapped to different memory modules.
The main changes:
  High order 30 address lines (A31-A2) are connected to memory modules.
  Low order two address lines (A1 and A0) are used to select one of the modules.

## Slide 13
How are the addresses mapped to memory modules?
  Module M0: 0, 4, 8, 12, 16, 20, 24, …
  Module M1: 1, 5, 9, 13, 17, 21, 25, …
  Module M2: 2, 6, 10, 14, 18, 22, 26, …
  Module M3: 3, 7, 11, 15, 19, 23, 27, …
Memory addresses are interleaved across memory modules.
What we can gain from this mapping?
  Consecutive addresses are mapped to consecutive modules.
  Possible to access four consecutive words in the same cycle, if all four modules are enabled simultaneously.

## Slide 14
Motivation for word alignment in MIPS32 data words.
  32-bit words start from a memory address that is divisible by 4.
    Corresponding byte addresses are (0, 1, 2, 3), (4, 5, 6, 7), (8, 9, 10, 11), (12, 13, 14, 15), etc.
    Possible to transfer all the four bytes of a word in a single memory cycle.
  What happens if a word is not aligned?
    Say: (1, 2, 3, 4) or (2, 3, 4, 5) or (3, 4, 5, 6).
    Two of the bytes will be mapped to the same memory module.
    Hence the word cannot be transferred in a single memory cycle.
2 memory cycles required

## Slide 15
MEMORY M0
(1G x 8)
MEMORY M1
(1G x 8)
MEMORY M2
(1G x 8)
MEMORY M3
(1G x 8)
MIPS32
PROCESSOR
A31 – A2
D7 – D0
2 x 4
Decoder
A0
A1
CS0’
CS1’
CS2’
CS3’
CS0’
RD/WR’
CS1’
RD/WR’
CS2’
RD/WR’
CS2’
RD/WR’
Still one module is selected at a time :: 8 bits data transfer per cycle.

## Slide 16
MEMORY M0
(1G x 8)
MEMORY M1
(1G x 8)
MEMORY M2
(1G x 8)
MEMORY M3
(1G x 8)
MIPS32
PROCESSOR
A31 – A2
D31 – D0
2 x 4
Decoder
A0
A1
CS0’
CS1’
CS2’
CS3’
0
RD/WR’
0
RD/WR’
0
RD/WR’
0
RD/WR’
Enable all the four modules together.
32-bit parallel data transfer.

## Slide 17: Memory Latency and Bandwidth
Memory Latency:
  The delay from the issue of a memory read request to the first byte of data becoming available.
Memory Bandwidth:
  The maximum number of bytes that can be transferred between the processor and the memory system per unit time.

## Slide 18
Example 1:
  Consider a memory system that takes 20 ns to service the access of a single 32-bit word.
    Latency L = 20 ns per 32-bit word.
    Bandwidth BW = 32 / (20 x 10-9) = 200 Mbytes per second.
Example 2:
  The memory system is modified to accept a new (still 20ns) request for a 32-bit word every 5 ns by overlapping requests.
    Latency L = 20 ns per 32-bit word (no change).
    Bandwidth BW = 32 / (5 x 10-9) = 800 Mbits per second.