## Slide 1: Hardware Design Overview

## Slide 2
Digital Design Flow in FPGA
Architecture Design
Hardware Description
Behavioral Simulation
Synthesis
Implementation
Bitfile

## Slide 3
Digital Design Flow in FPGA
Architecture Design
Hardware Description
Behavioral Simulation
Synthesis
Implementation
Bitfile
Architecture Diagram

## Slide 4
Digital Design Flow in FPGA
Architecture Design
Hardware Description
Behavioral Simulation
Synthesis
Implementation
Bitfile
Architecture Diagram
Writing the HDL

## Slide 5
Digital Design Flow in FPGA
Architecture Design
Hardware Description
Behavioral Simulation
Synthesis
Implementation
Bitfile
Architecture Diagram
Writing the HDL
Functional Correctness

## Slide 6
Digital Design Flow in FPGA
Architecture Design
Hardware Description
Behavioral Simulation
Synthesis
Implementation
Bitfile
Architecture Diagram
Writing the HDL
Functional Correctness
Netlist Generation

## Slide 7
Digital Design Flow in FPGA
Architecture Design
Hardware Description
Behavioral Simulation
Synthesis
Implementation
Bitfile
Architecture Diagram
Writing the HDL
Functional Correctness
Netlist Generation
Place & Route

## Slide 8
Digital Design Flow in FPGA
Architecture Design
Hardware Description
Behavioral Simulation
Synthesis
Implementation
Bitfile
Architecture Diagram
Writing the HDL
Functional Correctness
Netlist Generation
Place & Route
FPGA Programming

## Slide 9: Multiplexer Built From Primitives
module mux(f, a, b, sel);
output f;
input a, b, sel;
and g1(f1, a, nsel),
g2(f2, b, sel);
or g3(f, f1, f2);
not g4(nsel, sel);
endmodule
a
b
sel
f
nsel
f1
f2
g1
g2
g3
g4
Verilog programs built from modules
Each module has an interface
Module may contain structure: instances of primitives and other modules

## Slide 10
module mux(f, a, b, sel);
output f;
input a, b, sel;
and g1(f1, a, nsel),
g2(f2, b, sel);
or g3(f, f1, f2);
not g4(nsel, sel);
endmodule
a
b
sel
f
nsel
f1
f2
g1
g2
g3
g4
Identifiers not explicitly defined default to wires
Multiplexer Built From Primitives

## Slide 11
module mux(f, a, b, sel);
output f;
input a, b, sel;
reg f;
always @(a or b or sel)
if (sel) f = b;
else f = a;
endmodule
a
b
sel
f
Modules may contain one or more always blocks
Sensitivity list contains signals whose change triggers the execution of the block
Multiplexer Built With Always

## Slide 12
module mux(f, a, b, sel);
output f;
input a, b, sel;
reg f;
always @(a or b or sel)
if (sel) f = b;
else f = a;
endmodule
a
b
sel
f
A reg behaves like memory: holds its value until imperatively assigned otherwise
Body of an always block contains traditional imperative code
Multiplexer Built With Always

## Slide 13
module mux(f, a, b, sel);
output f;
input a, b, sel;
assign f = sel ? b : a;
endmodule
a
b
sel
f
LHS is always set to the value on the RHS
Any change on the right causes re-evaluation
The infamous error: "concurrent assignment to a non-net is not permitted"
Mux with Continuous Assignment

## Slide 14
Any Sequence of letter, digits, dollar sign, underscore.
First character must be a letter or underscore.
It cannot be a dollar sign.
Cannot use characters such as hyphen, brackets, or # in verilog names
Identifiers in Verilog

## Slide 15
Predefined logic value system or value set
: ‘0’, ‘1’ ,’x’ and ‘z’;
‘x’ means uninitialized or unknown logic value
‘z’ means high impedance value.
Verilog Logic Values

## Slide 16
Nets: wire, supply1, supply0
  wire:
i) Analogous to a wire in an ASIC.
ii) Cannot store or hold a value.
Integer: used for the index variables of say for loops. No hardware implication.
Verilog Data Types

## Slide 17
The reg Data Type
Register Data Type: Comparable to a variable in a programming language.
Default initial value: ‘x’
module reg_ex1;
reg Q; wire D;
always @(posedge clk) Q=D;
A reg is not always equivalent to a hardware register, flipflop or latch.
module reg_ex2; // purely combinational
reg c;
always @(a or b) c=a|b;
endmodule

## Slide 18: Difference between driving and assigning
Programming languages provide variables that can contain arbitrary values of a particular type.
They are implemented as simple memory locations.
Assigning to these variables is the simple process of storing a value into the memory location.
Verilog reg operates in the same way. Previous assignments have no effect on the final result.

## Slide 19: Example
module assignments;
reg R;
initial R<=#20 3;
initial begin
R=5; R=#35 2;
end
initial begin
R<=#100 1;
#15 R=4;
#220;
R=0;
end
endmodule
The variable R is shared by all the concurrent blocks.
R takes the value that was last assigned.
This is like a hardware register which also stores the value that was last loaded into them.
But a reg is not necessarily a hardware register.

## Slide 20: Wire: helps to connect
Consider a set of tristate drivers connected to a common bus.
The output of the wire depends on all the outputs and not on the last one.
To model connectivity, any value driven by a device must be driven continuously onto that wire, in parallel with the other driving values.

## Slide 21: Code
module simple(A,B,C,sel,Z);
input A, B, C;
input [1:0] sel;
output Z;
reg Z;
always @(A or B or C or SEL)
begin
2’b00: Z=1’bz;
2’b01: Z=A;
2’b10: Z=B;
2’b11: Z=C;
endcase
end
endmodule
module simple(A,B,C,sel,Z);
input A, B, C;
input [1:0] sel;
output Z;
assign Z=(SEL==2’b01)?A: 1’bz;
assign Z=(SEL==2’b10)?B:1’bz;
assign Z=(SEL==2’b11)?C:1’bz;
endmodule
Inferred as a multiplexer.
But we wanted drivers!

## Slide 22: Code
module tristate_bus (
input wire enable1, enable2,
input wire [7:0] data1, data2,
output wire [7:0] bus
);
assign bus = enable1 ? data1 : 8'bz; // Tristate driver 1
assign bus = enable2 ? data2 : 8'bz; // Tristate driver 2
endmodule
If enable1 is 1 and enable2 is 0, bus takes data1.
If enable2 is 1 and enable1 is 0, bus takes data2.
If both enable signals are 1 and data1 ≠ data2, the bus enters an undefined (x) state due to contention.

## Slide 23: Code
module tristate_bus (
input [7:0] data1, data2,
output [7:0] bus
);
assign bus = data1
assign bus = data2
endmodule
Error: "Net out_signal has multiple drivers."

## Slide 24: Code
module multi_driver_error (
input wire clk,
input wire rst,
output reg out_signal
);
always @(posedge clk) begin
if (rst)
out_signal <= 0; // First driver
end
always @(posedge clk) begin
out_signal <= 1; // Second driver (Conflicting)
end
endmodule
Error: "Signal out_signal has multiple drivers. "

## Slide 25: Code
module multi_driver_fix (
input wire clk,
input wire rst,
output reg out_signal
);
always @(posedge clk) begin
if (rst)
out_signal <= 0;
else
out_signal <= 1;
end
endmodule

## Slide 26
Format of integer constants:
Width’ radix value;
Verilog keeps track of the sign if it is assigned to an integer or assigned to a parameter.
Once verilog looses sign the designer has to be careful.
Numbers

## Slide 27
Module interface provides the means to interconnect two verilog modules.
Note that a reg cannot be an input/ inout port.
A module may instantiate other modules.
Hierarchy

## Slide 28: Instantiating a Module
Instances of
module mymod(y, a, b);
Lets instantiate the module,
mymod mm1(y1, a1, b1); // Connect-by-position
mymod mm2(.a(a2), .b(b2), .y(c2)); // Connect-by-name

## Slide 29: Instantiating a Module
module top_module;
reg [3:0] x, y;
wire [3:0] result;
adder4 uut (x, y, result);
initial
begin
x = 4'b0011;
y = 4'b0101;
#10;
end
endmodule
module top_module;
reg [3:0] x, y;
wire [3:0] result;
adder4 uut (.a(x), .b(y), .sum(result));
initial
begin
x = 4'b0011;
y = 4'b0101;
#10;
end
endmodule
module adder4 ( input [3:0] a, input [3:0] b, output [3:0] sum );
assign sum = a + b;
endmodule

## Slide 30: Sequential Blocks
Sequential block is a group of statements between a begin and an end.
A sequential block, in an always statement executes repeatedly.
Inside an initial statement, it operates only once.

## Slide 31: Procedures
A Procedure is an always or initial statement or a function.
Procedural statements within a sequential block executes concurrently with other procedures.

## Slide 32: Assignments
module assignments
// continuous assignments
always // beginning of a procedure
begin //beginning of a sequential block
//….Procedural assignments
end
endmodule
A Continuous assignment assigns a value to a wire like a real gate driving a wire.
module holiday_1(sat, sun, weekend);
input sat, sun; output weekend;
// Continuous assignment
assign weekend = sat | sun;
endmodule
module holiday_2(sat, sun, weekend);
input sat, sun; output weekend;
reg weekend;
always @(sat or sun)
weekend = sat | sun; // Procedural
endmodule // assignment

## Slide 33: Blocking and Nonblocking Assignments
Blocking procedural assignments must be executed before the procedural flow can pass to the subsequent statement.
A Non-blocking procedural assignment is scheduled to occur without blocking the procedural flow to subsequent statements.

## Slide 34: Nonblocking Statements are odd!
a = 1;
b = a;
c = b;
Blocking assignment:
a = b = c = 1
a <= 1;
b <= a;
c <= b;
Nonblocking assignment:
a = 1
b = old value of a
c = old value of b

## Slide 35: Nonblocking Looks Like Latches
RHS of nonblocking taken from latches
RHS of blocking taken from wires
a = 1;
b = a;
c = b;
a <= 1;
b <= a;
c <= b;
1
a
b
c
“
”
a
b
c
1
“
”

## Slide 36: Examples
Blocking:
always @(A1 or B1 or C1 or M1)
begin
M1=#3(A1 & B1);
Y1= #1(M1|C1);
end
Non-Blocking:
always @(A2 or B2 or C2 or M2)
begin
M2<=#3(A2 & B2);
Y2<=#1(M1 | C1);
end
Statement executed at time t+3 causing Y1 to be assigned at time t+4
Statement executed at time t causing Y2 to be assigned at time t+1. Uses old values.
Statement executed at time t causing M1 to be assigned at t+3
Statement executed at time t causing M2 to be assigned at t+3

## Slide 37: Order dependency of Concurrent Statements
Order of concurrent statements does not affect how a synthesizer synthesizes a circuit.
It can affect simulation results.

## Slide 38: Order dependency of Concurrent Statements
always @(posedge clock)
begin: CONCURR_1
Y1<=A;
end
always @(posedge clock)
begin: CONCURR_2
if(Y1) Y2=B; else Y2=0;
end
B
A
clk
Y1
Y2
Can you figure out the possible mismatch of simulation with synthesis results?

## Slide 39: Explanation of the mismatch
The actual circuit is a concurrent process.
The first and second flip flop are operating parallel.
However if the simulator simulates CONCURR_1 block before CONCURR_2, we have an error. Why?
So, how do we solve the problem?

## Slide 40: Solution
always @(posedge clock)
begin
Y1<=A;
if(Y1==1)
Y2<=B;
else
Y2<=0;
end
With non-blocking assignments
the order of the assignments
is immaterial…

## Slide 41: Parameterized Design
module vector_and(z, a, b);
parameter cardinality = 1;
input [cardinality-1:0] a, b;
output [cardinality-1:0] z;
wire [cardinality-1:0] z = a & b;
endmodule
We override these parameters when we instantiate the module as:
module Four_and_gates(OutBus, InBusA, InBusB);
input [3:0] InBusA, InBusB; output[3:0] OutBus;
Vector_And #(4) My_And(OutBus, InBusA, InBusB);
endmodule

## Slide 42: Functions (cont’d)
Function Declaration and Invocation
  Declaration syntax:
    function <range_or_type> <func_name>;
    <input declaration(s)>
    <variable_declaration(s)>
    begin // if more than one statement needed
    <statements>
    end // if begin used
    endfunction

## Slide 43: Function Examples Controllable Shifter
module shifter;
`define LEFT_SHIFT 1'b0
`define RIGHT_SHIFT 1'b1
reg [31:0] addr, left_addr, right_addr;
reg control;
initial
begin
…
end
always @(addr)begin
left_addr =shift(addr, `LEFT_SHIFT);
right_addr =shift(addr,`RIGHT_SHIFT);
end
function [31:0]shift;
input [31:0] address;
input control;
begin
shift = (control==`LEFT_SHIFT) ?(address<<1) : (address>>1);
end
endfunction
endmodule

## Slide 44
Architecture Design
Algorithm
Hardware Design Architecture
Design Datapath Elements
Design Control Path

## Slide 45
Architecture Design
Algorithm of the Accumulator
# Accumulator Algorithm accumulator = 0
# Loop for N data inputs input_data = get_input() # Fetch new data
accumulator += input_data # Accumulate (accumulator = accumulator + input_data)
# Output the final accumulated value print(accumulator)
Adder
Reg
Input_data(4 bits)
dff_out
add_out
acc
clk
rst
(5 bits)
(5 bits)
(5 bits)
Hardware Design Architecture of the Accumulator

## Slide 46
Architecture Design
Algorithm of the Accumulator
# Accumulator Algorithm accumulator = 0
# Loop for N data inputs input_data = get_input() # Fetch new data
accumulator += input_data # Accumulate (accumulator = accumulator + input_data)
# Output the final accumulated value print(accumulator)
Adder
Reg
Input_data(4 bits)
dff_out
add_out
acc
clk
rst
(5 bits)
(5 bits)
(5 bits)
Hardware Design Architecture of the Accumulator

## Slide 47
Architecture Design
Algorithm of the Accumulator
# Accumulator Algorithm accumulator = 0
# Loop for N data inputs input_data = get_input() # Fetch new data
accumulator += input_data # Accumulate (accumulator = accumulator + input_data)
# Output the final accumulated value print(accumulator)
Adder
Reg
Input_data(4 bits)
dff_out
add_out
acc
clk
rst
(5 bits)
(5 bits)
(5 bits)
Hardware Design Architecture of the Accumulator

## Slide 48
Architecture Design
Algorithm of the Accumulator
Hardware Design Architecture of the Accumulator
# Accumulator Algorithm accumulator = 0
# Loop for N data inputs input_data = get_input() # Fetch new data
accumulator += input_data # Accumulate (accumulator = accumulator + input_data)
# Output the final accumulated value print(accumulator)
Accumulator
Adder
Reg
Input_data(4 bits)
clk
rst
acc

## Slide 49
Datapath Element Design
Ripple Carry Adder
Carry Look Ahead Adder

## Slide 50
Datapath Element Design
Ripple Carry Adder
Carry Look Ahead Adder
Pros:
Much faster than RCA, especially for wide adders.
Parallel carry computation reduces critical path delay.
Cons:
More complex design (requires additional logic for generate/propagate).
Higher area and power consumption due to extra gates.
Pros:
Simple design and easy to implement.
Low area and power consumption for small bit-width adders.
Cons:
Slow for large bit-widths due to the sequential carry propagation (linear delay).
Propagation Delay: Increases linearly with the number of bits.

## Slide 51
Datapath Element Design
Ripple Carry Adder
Carry Look Ahead Adder
Pros:
Much faster than RCA, especially for wide adders.
Parallel carry computation reduces critical path delay.
Cons:
More complex design (requires additional logic for generate/propagate).
Higher area and power consumption due to extra gates.
Pros:
Simple design and easy to implement.
Low area and power consumption for small bit-width adders.
Cons:
Slow for large bit-widths due to the sequential carry propagation (linear delay).
Propagation Delay: Increases linearly with the number of bits.
Critical Path

## Slide 52
For each bit i (i = 0 to 3):
A[i], B[i]: Input bits
G[i] = A[i] · B[i] → Generate
P[i] = A[i] ⊕ B[i] → Propagate
CLA Carry Equations
Given C0 as the input carry:
C1 = G0 + (P0 · C0)
C2 = G1 + (P1 · G0) + (P1 · P0 · C0)
C3 = G2 + (P2 · G1) + (P2 · P1 · G0) + (P2 · P1 · P0 · C0)
C4 = G3 + (P3 · G2) + (P3 · P2 · G1) + (P3 · P2 · P1 · G0) + (P3 · P2 · P1 · P0 · C0)

## Slide 53: How Are Simulators Used?
Testbench generates stimulus and checks response
Coupled to model of the system
Pair is run simultaneously
Testbench
System Model
Stimulus
Response
Result checker

## Slide 54: Looking back at our multiplexer
“Dataflow” Descriptions of Logic
//Dataflow description of mux
module mux2 (in0, in1, select, out);
input in0,in1,select;
output out;
assign out = (~select & in0)
| (select & in1);
endmodule // mux2
Alternative:
assign out = select ? in1 : in0;

## Slide 55: TestBench of the Multiplexer
Testbench
module testmux;
reg a, b, s;
wire f;
reg expected;
mux2 myMux (.select(s), .in0(a), .in1(b), .out(f));
initial begin
$dumpfile("wave.vcd");
$dumpvars(0, testmux);
end
initial
begin
s=0; a=0; b=1; expected=0;
#10 a=1; b=0; expected=1;
#10 s=1; a=0; b=1; expected=1;
end
initial
$monitor(
"select=%b in0=%b in1=%b out=%b, expected out=%b time=%d",
s, a, b, f, expected, $time);
endmodule // testmux

## Slide 56
Thank You